# 2nd notes for - Beginning c++17 From Novice to Professional
### Chapter 5 Arrays and Loops
#### Container
##### array<>s
  - std::array<data_type,number>
  - std::array<..> is a container templates that lets you initialise a container object that behave like a standard c-array but with added security measures(range checks ::at(i), easy acces to size of the array ::size()) and comfortability (first element by array.front(), last element with array.back() etc.).
  - Array.at(i) works like array[i] but does an implicit range check and therefore avoids errors if i is out of the the array<>s range (or negative).
  - Array.size() access the size of the array<>
  - array.fill(n) sets all the array<> members to the value n.
  - Array.front() acces first array<> element . Equals array[0]
  - array.back() access last array<> element. Equals array[array.size()-1]
  - array<> objects can also be stored in containers:
    - std::vector<std::array<int,100> vector_of_int_arrays;
  - array<> elements are implicitly initialised!
  - Passing array<>s to functions is straightforward!
##### vector
- is a sequence container!
- Number of elements can be varied dynamically. Does not need to be set at initialisation
- New elements are automatically initialised with zero if no value is specified
- passing vector<>s to functions is straightforward.
- Two vectors can be compared using "<", ">", "<=", ">=", "==", and "!=" operators!
  - Uses lexicographical comparison. "aardvark" before "zombie"
- Has familiar functions
  - front()
  - back()
  - size()
- assignment of one vector<> to another, copies all elements overwriting possible preceding infromation
- vector<>s can be stored inside containers.
- Assign() function can be used to reinitialize elements of the vector! No fill() function for vector.
  - Std::vector<long> vector1(20,99L) // vector1 contains 20 long data with the value '99L'
  - vector1.assign(3,20L) //vector1 now contains only 3 elements. Both have the Value 99.
  - vector1.assign({99L,20L}) // vector1 now contains 2 elements. '99' and '20'.
- .clear() Function removes all elements of a vector!
- .push_back(<value>) creates and adds an element at the end of the vector sequence container.
- .pop_back() removes the last element of a vector.
- .empty() returns if the vector is empty.